## Slide 1: ECE GY 6913 Computing Systems Architecture
RISCV Simulator Project – Phase 1 Fall 2024

## Slide 2: Goal of the Project
Have a working model of a 32 bit RISC-V interpreter.
Accurately maintain the values in all registers and memory locations.
Project is to be done either in Python or C++. The boiler-plate code will been provided on brightspace.
Project is to be done individually.

## Slide 3: Grading Scheme and support
Weightage of the RISCV project will be 10% of your total grade.
Each phase (Single stage and Five stage) will be out of 50 marks
Test cases – total 10 – 3 of which will be released a week before submission of each phase.
Project report – contains questions and marking scheme which will be posted on Brightspace
Mondays 9:00 AM – 11:30 AM will be project office hours starting 7th Oct 2024
Phase 1 submission is on 8th Nov 2024

## Slide 4: Input
imem.txt
contains binary input of all the instructions
dmem.txt
contains binary input of all the memory locations

## Slide 5: Output
Performance Metrics
Register States after each cycle
DMem at the end of program execution
State Results

## Slide 6: What needs to be done in IF
Read 4 lines of the IMEM file.

## Slide 7: What needs to be done in ID
Convert the 32 bits into an instruction. (Big endian)
00000000
01010010
00000001
10110011
Instruction: 00000000010100100000000110110011
Decoded instruction: add x3, x4, x5

## Slide 8: What needs to be done in EX
Instruction: add x3, x4, x5
lw x10, 20(x12)
Be sure to perform the right execution at this stage.
R and I type instructions will perform the normal executions.
Load and Store instructions will perform calculations of offset.

## Slide 9: What needs to be done in MEM
Make sure to access memory in this stage.
LOAD and STORE instructions

## Slide 10: What needs to be done in WB
Update the values of registers in this stage.
Eg. loading a value into a register, arithmetic result to be written into register

## Slide 11: Instructions to be implemented
Please refer Brightspace Project document which contains all instructions that need to be implemented.